## Slide 1: MATISSE Data Reduction
A. Meilland, P Berio, F. Millour and the MATISSE consortium

## Slide 2
MATISSE Data Reduction Software
  MATISSE Pipeline developed in C with ESO Standard
  including CPL, GSL, FFTW, FITSIO, ERFA
  MATISSE Recipes run through ESOREX :
    directly in command line
    with ESO interactive tools
      REFLEX
      GASGANO
    with the consortium Python package (mat_tools)
      In command line
      Interactively

## Slide 3
MATISSE Data Reduction Software
  mat_raw_estimates : computes raw interferometric observables
    (square visibility & coherent flux, closure phase, differential phase)
      Produce OIFITS files for raw data
  mat_cal_oifits : calibrates raw interferometric observables (SCI /CAL)
    Produce OIFITS files for calibrated data
  mat_cal_imarec : reconstructs an image from serie of OIFITS files
        Use IRBIS algorythm

## Slide 4
MATISSE Data Reduction Software
  mat_raw_estimates :
    mat_cal_image : raw image calibration
    mat_ext_beams : photometric estimation
    mat_est_corr : correlated flux estimation
    mat_est_opd : OPD estimation
    mat_proc_incoherent : incoherent processing
    mat_proc_coherent : coherent processing
    mat_est_tf : transfert function estimation
    mat_merge_results : merge intermediate products into OIFITS files

## Slide 5
MATISSE Data Reduction Software
1D-FFT Modulus
RAW Fringes
RAW Fringes
1D-FFT Phase
SKY
STATIC CAL.
BPM + FFM
SHIFT
+
BIAS
Corr. Flux
Differential Phase (OI_VIS)
Closure Phase (OI_T3)
V² (OI_VIS2)
Photometric beams
Flux (OI_FLUX)

## Slide 6
MATISSE Data Reduction Software
Incoherent integration
Frame integration in two different modes
Coherent integration
AMBER like
Per frame OPD
OPD correction
Coherent Integration
MIDI like
OPD and ϕachromatic phase per frame
Correaction OPD and ϕachromatic
Coherent integration
ϕdiff
Vdiff
Vis or Corr. Flux
ϕdiff

## Slide 7
MATISSE Data Reduction Software
About the Photometry in Hybrid mode
L&M bands : SIPHOT
N band : HISENS
Hybrid sequence of observation

## Slide 8
MATISSE Data Reduction Software
To Chop or not to Chop?
N-band
No Chopping

No Photometry

No visibility
(only Corr. Flux)
LM-bands
No Chopping

No Chopped Fringes

Bad photometry
for Fainter Targets
(limit depends on λ)

Bad visibility
(Corr. Flux not affected)

## Slide 9
MATISSE Data Reduction Software
To Chop or not to Chop
Non-chopped (blue) diverges at 3.7um for this 14 Jy source
Consortium working on that issue (possibility to always chop)

## Slide 10
MATISSE Data Reduction Software
The BCD sequence and its consequences
 | OUT-OUT | IN-OUT | OUT-IN | IN-IN
Peak1 | U3-U4 | U4-U3 | U3-U4 | U4-U3
Peak2 | U1-U2 | U1-U2 | U2-U1 | U2-U1
Peak3 | U2-U3 | U2-U4 | U1-U3 | U2-U3
Peak4 | U2-U4 | U2-U3 | U1-U2 | U1-U3
Peak5 | U1-U3 | U1-U4 | U2-U3 | U2-U4
Peak6 | U1-U4 | U1-U3 | U2-U4 | U2-U3
U1
U2
U3
U4
BCD2
BCD1
P1 P2 P3 P4 P5 P6
Effects in final OIFITS files :
Swap baselines between exposures
Inverse telescopes for some baselines
Effect on closure phase too (3 Tels)
Exposure merging is not trivial!
FFT

## Slide 11
MATISSE Data Reduction Software
Data calibration : V²
Vcalibrator
Transfer function
TF =
Vscience
V =
Angular stellar diameter θ
from JSDC catalog
TF

## Slide 12
MATISSE Data Reduction Software
Data calibration : Closure phase ( and differential phase)
CPscience
-CPscience (BCD swap)
CPcalibrator
CP = CPscience - CPcalibrator
Computed in complex number
Same for differential phase

## Slide 13
MATISSE Data Reduction Software
Data calibration : MATISSE data are spectro-interferometric
Rigel V² contaminated by spectral features from calibrator ψ Phe

## Slide 14
MATISSE Data Reduction Software
Reducing data with ESOREX

## Slide 15
MATISSE Data Reduction Software
ESOREX mat_raw_estimates recipe options
esorex --man-page mat_raw_estimates

## Slide 16
MATISSE Data Reduction Software
ESOREX mat_raw_estimates recipe sof file
Observations
Calibrations

## Slide 17
MATISSE Data Reduction Software
Quick view on the REFLEX GUI

## Slide 18
MATISSE Data Reduction Software
Quick view on the REFLEX GUI

## Slide 19
MATISSE Data Reduction Software
Quick view on the REFLEX GUI

## Slide 20
MATISSE Data Reduction Software
The consortium python tools
    https://gitlab.oca.eu/MATISSE/tools/
Download and installation instruction on the OCA gitlab repository

## Slide 21
MATISSE Data Reduction Software
The consortium python tools
Data reduction:
mat_autoPipeline.py : produces raw oifits file for a all raw data in a directory
mat_tidyupOiFits.py : renames data files after mat_automaticPipeline.py
mat_autoCalib.py : produces calibrated data from raw oifits files.
mat_logger.py : GUI allowing to perform reduction in an interactive way
Data visualization:
mat_show_oifits.py: Interactive plotting tools from MATISSE OiFits data (raw and calibrated)
mat_showOiData.py: AMBER like summary plot of one OiFits file (Flux, V², ϕdiff, CP, Telescopes config)
mat_showOiFreq.py: V² and CP plotted as a function of the spatial frequency (B/λ )
mat_showTransFunc.py: Transfer function plot
Post-tools (upcoming) :
mat_mergeByTPLStart.py : merge all exposure of observation ( 4 in N and 4 or 12 in LM)
mat_spectralBinning.py : binning pixels into spectral channels (3 in LM and 5 in N)
Mar_spectralSmoothing.py : smooth on spectral channel instead of binning (produces more MIDI like data

## Slide 22
MATISSE Data Reduction Software
mat_autoPipeline.py

## Slide 23
MATISSE Data Reduction Software
mat_autoPipeline.py
Produce all SOF files for data reductions
Example of MATISSE sof file for mat_raw_estimate recipe
Intermediate an final products from data reduction

## Slide 24
MATISSE Data Reduction Software
mat_tidyupOiFits.py : Copy and rename OiFits files

## Slide 25
MATISSE Data Reduction Software
mat_logger.py GUI:
Logging tools but also
Interactive data reduction
visualization of raw files

## Slide 26
MATISSE Data Reduction Software
mat_logger.py GUI:
Launch mat_autoPipeline.py + mat_tidyupOifits.py
on selected Obs only (selected options)
Redirect data reduction logs into file.
Can be launch again using a sh script

## Slide 27
MATISSE Data Reduction Software
mat_show_oifits.py GUI:
Transfer Function
V² as function of λ

## Slide 28
MATISSE Data Reduction Software
Examples of plots : mat_showOiData.py

## Slide 29
MATISSE Data Reduction Software
Examples of plots : mat_showOiData.py
Tribute to AmdlibShowOiData

## Slide 30
MATISSE Data Reduction Software
Examples of plots : mat_showOiFreq.py

## Slide 31
MATISSE Data Reduction Software
Examples of plots : mat_showTransFunc.py

## Slide 32
MATISSE Data Reduction Software
Upcoming post-tools : mat_mergeByTPLStart.py
One single calibrated measurement on the B[e] star MWC300
4 exposures in N
12 exposures in L

## Slide 33
MATISSE Data Reduction Software
Upcoming post-tools : mat_mergeByTPLStart.py
Merging after correcting BCD sequence  SNR enhanced by 3.5 in L and 2 in N

## Slide 34
MATISSE Data Reduction Software
Upcoming post-tools : mat_spectralBinning.py
Spectral binning a-posteriori  SNR enhanced by 2.2 (5px) in L and 2.6 (7px) in N

## Slide 35
MATISSE Data Reduction Software
DRS functional but still in development
Future Improvements in the pipeline:
“blind” Coherent integration using L band OPD for N
A-priori spectral binning/smoothing (MIDI-like)
GRA4MAT data (using K-band tracker information)
Frame selection to remove “bad frames”
Python tools improvements:
Post-tools (cutting, merging, binning, smoothing)
Improved data visualization
Spectrum and flux calibration
Interface to image reconstruction software IRBIS (currently in shell-scripts)
Don’t hesitate to contact us in Nice or at ESO